## Slide 1: CSPEC – The cold chopper spectrometer for the ESS
P.P. Deen,a,b F. Moreira,b,c L. Loaiza,a W. Lohstroh,a D. Norefini,b S. Longeville,c
a Heinz Maier-Leibnitz Zentrum (MLZ), Technische Universität München, Garching, Germany
b European Spallation Source (ESS), Lund, Sweden
c Laboratoire Leon Brillouin (LLB), France
European Spallation Source ESS
CSPEC – Cold Chopper Spectrometer
“The European Spallation Source (ESS) is a European Research Infrastructure Consortium (ERIC), a multi-disciplinary research facility based on the world’s most powerful neutron source. The unique capabilities of this new facility will both greatly exceed and complement those of today's leading neutron sources, enabling new opportunities for researchers across the spectrum of scientific discovery, including life sciences, energy, environmental technology, cultural heritage and fundamental physics.“ (ESS mission statement)
Leguy, Aurelien MA, et al., Nature communications 6 (2015).
hybrid organic-inorganic perovskite solar cells CH3NH3PbI3
L. E. Bove, S. Klotz, J. Philippe, and A. M. Saitta
Phys. Rev. Lett. 106, 125701 (2011)
high pressure ice
CSPEC characteristics
Wavelength range = 2 – 20 Å.
CSPEC shall probe excitations up from 0.005 up to 20 meV.
CSPEC shall measure in repetition rate multiplication configuration.
CSPEC shall be capable of energy resolutions down to ΔE/E = 1.5% at 4 Å
CSPEC shall be capable of spatial resolution ΔQ/Q = 2%.
CSPEC shall provide a signal to noise of 105 at 5 Å
The neutron beam at the sample position shall illuminate a sample area ranging from 4 x 2 cm2 to 1.0 x 1.0 cm2 (height x width)
CSPEC should follow kinetic processes with time steps of one minute.
Current status of the construction project
A. Khaplanov et al. (ESS)
The way to CSPEC
Sample detector distance = 3.5 m
detector angular coverage
5 – 140°horizontal
+/- 26.5°vertical (3.5 m height) (+/- 8 on day 1)
combined sample chamber & tank under vacuum (10-4 mbar)
gate window: sample environement at ambient conditions (Al window thickness 2-3 mm)
side access to sample chamber
Secondary Spectrometer & Detectors
10B multigrid detectors: performance
Instrument Suite
view of cold focal point of the butterfly moderator
vertical s-curved guide (radius of curvature 1600 m, loss of line-of-sight inside bunker at 26.53m)
horizontal curvature (R = 4000m) to compensate monolith insert rotation
elliptic opening / closing towards high speed choppers and sample position
< 10 % intensity variation across beam spot
4 x 2 cm2 beam spot (1 x1 cm2 in focused mode), height x width
divergence +/- 1 deg at 3 Å
smooth divergence profile
Beam Extraction and Guide Transport System – First deliveries
3.32 Å
Thank you
P. Link(TUM), F. Horn (TUM), H. Meier(TUM), A. Cazenave (LLB), S. Desert(LLB)., G. Fabreges (LLB) N. Tsapatsaris (ESS),R. Al Jebali (ESS), A. Kaphlanov (ESS) M. Anastasopoulos (ESS), G. Laszlo (ESS), C. Lopez (ESS)
4035 mm
4735 mm
4035 mm
4735 mm
In monolith NBOA
Inside bunker
E02
E01
Beam transport and conditioning system
Primary spectrometer
Experimental cave
Secondary spectrometer
D03
E02.2
BW3 & PSC chopper pit
Bunker wall Feedthrough
Collimation Vanes
Cd inner dressing
Detectors
Enlarged sample pot and access
Complying with SAD requirements
Main TOF chamber
Radial Collimator
Guide exchanger under development at LLB
High speed chopper
3 carbon fiber disks
Generous space for sample handling
Phase 1
Prelim Design
Phase 2
Detailed Design
Phase 3
Procurement & Start of Installation
Phase 4
Installation & cold commissioning
Phase 5
Hot commissioning
2017
2019
2020
2021
2023